## Slide 1: Multi-Objective Optimization: Principles and Algorithms
AE 6310: Optimization for the Design of Engineered Systems
Spring 2017
Dr. Glenn Lightsey
Lecture Notes Developed By Dr. Brian German

## Slide 2: Multi-Attribute Problems
So far, we have considered “single-objective” optimization problems in this class. These have the form:

## Slide 3: Multi-Attribute Problems
In many real-life problems, we are concerned with multiple attributes of a problem, for example:
  y1 = Cost
  y2 = Performance
  y3 = Manufacturability
  y4 = Safety
  y5 = Robustness
  …

## Slide 4: Multi-Attribute Problems
Multi-attribute problems may be optimized by defining a “utility function” or “value function” that aggregates the multiple attributes we care about into a single function.
If we can obtain such a function, it can serve as the objective function in one of the “single-objective” optimization techniques previously introduced in this class. Thus we can obtain a single “best” solution.

## Slide 5: Multi-Attribute Problems
E.g. f = 0.5y1 + 3/y2 + 0.7y3*y4 + y5
This approach may be called “a priori” multi-objective optimization.
The difficulty of this approach is that f must be chosen very carefully
For example, consider that each attribute likely has very different units. How do you combine “specific fuel consumption” with “mean time between failures” in a value function?

## Slide 6: Multi-Attribute Problems
This lecture is about “a posteriori” multi-objective optimization (which we will simply call “multi-objective optimization”)
In a posteriori multi-objective optimization, we do not combine the multiple attributes y1,…,yk into an aggregate objective function that has a single “best” or “optimal” solution
Instead, the goal of a posteriori multi-objective optimization is to generate a set of solutions, each of which represents some relative optimality between the competing attributes.
The “best” solution out of this set is then selected later as a separate exercise

## Slide 7: Multi-Attribute Problems

## Slide 8: Ordering Solutions
In “single-objective” optimization, any two designs, x1 and x2 can be compared, by using the objective function, to determine which is preferred (or that both are equally preferable)
The objective function therefore defines a “total order” on the feasible designs

## Slide 9: Ordering Solutions
Requirements for a total ordering
  Antisymmetry: If f(x1) ≤ f(x2) and f(x2) ≤ f(x1) then f(x1) = f(x2)
  Transitivity: If f(x1) ≤ f(x2) and f(x2) ≤ f(x3) then f(x1) ≤ f(x3)
  Totality: Either f(x1) ≤ f(x2) or f(x2) ≤ f(x1) (or both)
The third property, totality, ensures that we can compare ANY two designs with the objective function to determine which design is better (or that both are equally good).

## Slide 10: Ordering Solutions
Multi-objective optimization is based on a partial ordering
Partial orderings have the property that some elements (i.e. designs) may be compared, but others are incomparable.
The goal of multi-objective optimization is to find a set of designs that are better than all designs to which they can be compared, but that are incomparable to each other.
In principle, any partial ordering could be used for “multi-objective optimization.” However, in practice, the Pareto Dominance partial ordering is always used.

## Slide 11: Pareto Dominance
Which point(s) would you prefer?

## Slide 12: Pareto Dominance
Compared to B: A has a better value of y1 C has a better value of y1 & y2
If y1 and y2 are the only attributes we care about, there is no reason to choose B over either A or C
A has a better value of y1 than C, but C has a better value of y2. Since we haven’t specified any preference for relative optimality in y1 vs y2, A and C are incomparable.

## Slide 13: Pareto Dominance
We say that A “weakly dominates” B because it is better in some attributes and equal in others.
We say that C “strongly dominates” B because it is better in all attributes.
A and C are incomparable because A is better than C in some attributes but worse in others.
Pareto Dominance is a partial ordering because some points are incomparable.

## Slide 14: Definition of Pareto Dominance
Given: a design problem with scalar-valued attributes y1 ,… yk
Suppose that the objective is to minimize each attribute
Let A and B denote two different vectors of attribute values (i.e. two different points in the objective space)
Then A dominates B if and only if:
  A is no worse than B in all attributes y1,… yk
  A is better than B in at least one attribute (equivalently, A and B are not equal)
Note that if A is better than B in some attributes but worse in others, neither A nor B dominates the other (incomparable).

## Slide 15: Pareto Optimality
A point in the feasible objective space that is not dominated by any other point in the feasible objective space is called “non-dominated.” The corresponding design is called “Pareto optimal” or “Pareto efficient”
(Sometimes all three of these terms are used interchangeably)
A point is non-dominated if there are no other points in its “dominance cone” (the region to the lower left of the dashed lines in the figure)

## Slide 16: Pareto Frontiers
The subset that consists of all non-dominated points in a given set is called the set’s “Pareto Frontier.”
The Pareto Frontier is always a portion of the set’s “boundary.”
Points on the Pareto Frontier have the property that no attribute can be improved by moving from point to point without worsening at least one other attribute, i.e. the Pareto frontier describes necessary tradeoffs in optimality

## Slide 17: Pareto Frontier of a Continuous Set

## Slide 18: Pareto Frontier of a Discrete Set

## Slide 19: Pareto Frontier of a Concave Set

## Slide 20: Theory Summary
Multi-objective optimization is based on a weaker premise than single-objective optimization: partially ordering designs instead of totally ordering.
Because of this, multi-objective optimization is unable to identify a unique “best” solution to a problem.
Instead, a set of solutions is obtained, any of which might be considered the “best” for some defined preference for relative optimality among the competing attributes.

## Slide 21: Theory Summary
Multi-objective optimization is useful when a single objective function cannot be agreed upon a priori
The set of non-dominated designs obtained from multi-objective optimization can be examined by the designer in order to:
  Refine the optimization search space
  Formulate a single-objective optimization problem
  Select a best design
  Understand tradeoffs in the objective space and their causes
  …

## Slide 22: Multi-Objective Optimization
The goal of multi-objective optimization is to sample points from the Pareto frontier.
For continuous optimization problems, there are an infinite number of non-dominated points. Our goal is to find a discrete sampling that is representative of the Pareto frontier.
A “representative” sampling usually entails:
  Points are sampled from all regions of the Pareto frontier
  The sampled points are fairly evenly spaced along the Pareto frontier
  Enough points are sampled to fulfill some purpose

## Slide 23: Multi-Objective Optimization
Good Bad Bad

## Slide 24: Multi-Objective Optimization vs. Monte Carlo
Extent of objective space explored by (uniform) random sampling of a problem with 2 attributes and 12 independent variables:

## Slide 25: Multi-Objective Optimization Algorithms
There are two general strategies used by multi-objective optimization algorithms:
Define a series of “single-objective” subproblems such that the solution of each subproblem gives one point on the Pareto frontier. Subproblems may be defined by:
  Changing the objective function
  Changing the constraints
Simultaneously optimize a population of points to iteratively approach the true Pareto frontier.

## Slide 26: Pareto Filtering
The various multi-objective optimization approaches attempt to sample points on the Pareto frontier, but generally there is no guarantee that they will succeed.
As a final step to any multi-objective optimizer, a “Pareto filter” that removes any dominated points from the final sampling should be used. This filter just applies logical checks of the inequalities involved in the definition of dominance.

## Slide 27: Aggregate Objective Function Approach
One approach to multi-objective optimization is to define a “weighted” aggregate objective function of the form which may be used as the objective function in a “single-objective” optimization algorithm
Here wi represents a “weight” on each attribute such that the weights sum to 1.
By specifying different values for the weights, different subproblems are defined. Each subproblem is solved to sample a single point.
Typically the weights are selected to form an evenly spaced grid in the “weight space” with the hopes that this will yield an even sampling of the Pareto frontier.

## Slide 28: Aggregate Objective Function Approach
The aggregate objective function is used to form a single-objective optimization subproblem.
The subproblem also includes any constraints on the independent variables and/or attributes that the designer wishes to impose.

## Slide 29: Aggregate Objective Function Approach
A well-known pitfall of the AOF approach is that it can sample only from regions of the Pareto frontier whose curvature is greater or equal to the curvature of the AOF.
  See Messac et al. “Ability of objective functions to generate points on nonconvex Pareto frontiers” AIAA Journal 38, 2000
AOFs are generally convex, so this problem only affects concave Pareto frontiers.
Even with the required curvatures, AOFs often lead to irregular samplings of the frontier for an evenly spaced weight grid.

## Slide 30: Weighted p-norm
A common aggregate objective function is the weighted p-norm:
When p=1, this is simply a weighted sum of the attributes

## Slide 31: Weighted Sum Example
f(x) = 0.5y1(x) + 0.5y2(x)

## Slide 32: Weighted Sum Example
f(x) = 0.333y1(x) + 0.667y2(x)

## Slide 33: Weighted Sum Example
f(x) = 0.667y1(x) + 0.333y2(x)

## Slide 34: Weighted Sum Example

## Slide 35: Weighted Sum Example

## Slide 36: Epsilon-Constraint Method
An alternative to the aggregate objective function is to simply use one of the attributes as the objective function, while constraining the remaining attributes to be at least as good as some value.
By varying the values of these threshold constraints, different points on the Frontier are sampled.
This is called the “epsilon constraint method”.
For unusually shaped objective spaces, many subproblems will have no solution.
The similar “method of proper equality constraints” uses equality constraints instead of inequality constraints.

## Slide 37: Epsilon-Constraint Method
min (y2) s. t. y1 < a

## Slide 38: Epsilon-Constraint Method
min (y2) s. t. y1 < b

## Slide 39: Epsilon-Constraint Method
min (y2) s. t. y1 < c

## Slide 40: Epsilon-Constraint Method
min (y2) s. t. y1 < d

## Slide 41: Epsilon-Constraint Method
min (y2) s. t. y1 < e

## Slide 42: Normal Boundary Intersection
Normal Boundary Intersection was invented by Das and Dennis (1998) to yield more evenly spaced samplings of the Pareto frontier.
Similar to the epsilon-constraint method, NBI works by forming a series of subproblems, each of which has different constraints.
The constraints are more smartly defined in order to minimize the number of failed subproblems.
However, NBI has a characteristic inability to sample from regions near the edges of < 2-attribute Pareto frontiers

## Slide 43: Normal Boundary Intersection
Using an appropriate single-objective optimizer, find the k points that optimize each attribute individually, yi*
Form an evenly spaced simplex-grid of “basepoints” in the objective space by taking weighted sums of the individual optima: yj0 = w1 y1* + w2 y2* +…+ wk yk*
Compute the “utopia point” and “antiutopia point” by taking the best and worst attributes from the set {y1*, y2*, … , yk*}
The search direction is the vector from the antiutopia point to the utopia point.
For each basepoint, maximize the distance along this direction, while still remaining in the feasible objective space.

## Slide 44: Normal Boundary Intersection
u-

## Slide 45: Normal Boundary Intersection
u-

## Slide 46: Normal Boundary Intersection

## Slide 47: Normal Boundary Intersection
NBI is unable to sample from regions near the boundary of most Pareto frontiers involving 3 or more attributes.

## Slide 48: Normal Boundary Intersection

## Slide 49: (Normalized) Normal Constraint Method
Messac et al. invented the Normal Constraint Method, which is conceptually similar to NBI except that it…
  Replaces NBI’s equality constraint with several inequality constraints
  Locates the search basepoints such that they are guaranteed to cover the entire Pareto frontier. … But the basepoints are still uniformly distributed and this leads to many subproblems failing.
You will often see NNC mentioned in the same sentence as NBI

## Slide 50: (Normalized) Normal Constraint Method
Region
Searched
by NBI
Region
Searched
by NNC

## Slide 51: NSGA-II
The methods just described all sample the Pareto frontier by solving single-objective subproblems.
An alternative approach to multi-objective optimization is to use a multi-objective evolutionary algorithm (MOEA) to optimize a population of points that sample the Pareto frontier.
The most popular MOEA is NSGA-II (Non-Dominated Sorting Genetic Algorithm II)
NSGA-II was published by Deb et al. in 2002 and is used by the MATLAB function “gamultiobj”

## Slide 52: NSGA-II
Unlike the previously described algorithms, NSGA-II directly uses the concept of dominance to optimize the population.
NSGA-II’s “fitness function” is based on two quantities that are calculated for each population member at each iteration:
  Non-Domination Level – A measure of relative dominance
  Crowding Distance – A measure of relative isolation

## Slide 53: Non-Domination Levels
Non-domination levels generalize the idea of “dominated” vs. “non-dominated” to integer valued levels that indicate how dominated each population member is relative to the other population members.
Non-domination level of 0 indicates that a population member is non-dominated.
Higher non-domination levels indicate increasingly higher levels of dominance (i.e. further from the Pareto frontier)

## Slide 54: Non-Domination Levels
Assign all non-dominated population members to level 0.
“Set aside” these points and consider only the remaining population members
Assign all non-dominated members of this remaining subset to level 1.
Set aside these points…
Repeat until all population members have been assigned to a level.

## Slide 55: Crowding Distance
Crowding distance is a measure of how isolated each point in the population is.
By preferring more isolated points, i.e. those with the largest crowding distance, the final sampling becomes more evenly spaced.
Crowding distance is only calculated among population members of the same non-domination level. A point’s crowding distance is unaffected by points on higher and lower non-domination levels.

## Slide 56: Crowding Distance

## Slide 57: Crowding Distance

## Slide 58: Crowding Distance
Among the set, I, of points with non-domination level Fi
Number of points in I
Sort according to this attribute
Points with min/max of each attribute have infinite crowding distance so they are always preferred

## Slide 59: NSGA-II Algorithm
Begin with n randomly generated population members
For each generation, t:
  Begin with the population, P(t), of size n
  Perform crossover and mutation to generate a new population, Q(t)
  Append Q(t) to P(t) to yield a 2n member population, R(t)
  Calculate the attribute values y1,…,yk for all points in R(t)
  Calculate non-domination levels of R(t)
  Determine the maximum non-domination level of R(t) such that fewer than n points have a non-domination level strictly lower than this. (This limit may be level 0). Call this level Flimit and let m denote the number of points with level <Flimit.

## Slide 60: NSGA-II Algorithm
  Copy the m points with level <Flimit to the next iteration’s population, P(t+1)
  Copy the n-m points in level Flimit with the largest crowding distance to P(t+1) (Note that by definition, level Flimit contains at least n-m points)
  P(t+1) now contains exactly n points, and the next iteration begins.
Note that the crowding distance is only used for points on level Flimit and does not need to be calculated for points on other non-domination levels

## Slide 61: NSGA-II Algorithm
n
2n

## Slide 62: NSGA-II Algorithm
Note that each iteration considers the “parent” population alongside the “children” formed by crossover/mutation.
This is called an “elitist” approach because it ensures that the very best designs may be carried through every iteration.
Because of this, there is no incentive to not crossover or mutate every population member.
Consequently crossover and mutation fractions should be chosen to be quite high (e.g. 0.8), or the algorithm may be coded so that every population member is either mutated or used in a crossover operation.

## Slide 63: Constrained NSGA-II
A simple method of enforcing constraints is that for constrained optimization, add (the largest non-domination level + 1) to the calculated non-domination level of each infeasible population member.
E.g. if the largest non-domination level for the entire population is 6, an infeasible population member whose non-domination level is 3 would be assigned an effective non-domination level of 10.
Note that this method does not indicate how infeasible the population member is. More complicated “penalty functions” could be used to better guide the population toward the feasible design space.

## Slide 64: NSGA-II Example

## Slide 65: NSGA-II Example

## Slide 66: NSGA-II Example

## Slide 67: References
Multi-objective KKT Conditions (not covered in this lecture)
  Kuhn, H. W. & Tucker, A. W. Nonlinear Programming Proceedings of the Second Berkeley Symposium on Mathematical Statistics and Probability, University of California Press, Berkeley, 1951
Weighted Sum Method (not the original source of this method)
  Das, I. & Dennis, J. A closer look at the drawbacks of minimizing weighted sums of objectives for Pareto set generation in multicriteria optimization problems Structural Optimization, 1997, 14, 63-69

## Slide 68: References
Epsilon Constraint Method
  Haimes, Y. Y.; Lasdon, L. S. & Wismer, D. A. On a Bicriterion Formulation of the Problems of Integrated System Identification and System Optimization IEEE Transactions of Systems, Man, and Cybernetics, 1971, 1, 296-297
Normal Boundary Intersection
  Das, I. & Dennis, J. Normal-boundary intersection: A new method for generating the pareto surface in nonlinear multicriteria optimization problems SIAM Journal of Optimization, 1998, 8, 631-657
Normalized Normal Constraint Method
  Messac, A. & Mattson, C. A. Normal constraint method with guarantee of even representation of complete pareto frontier AIAA Journal, 2004, 42, 2101 - 2111

## Slide 69: References
NSGA-II
  Deb, K.; Pratap, A.; Agarwal, S. & Meyarivan, T. A fast and elitist multiobjective genetic algorithm: NSGA-II IEEE Transactions on Evolutionary Computation, 2002, 6, 182 - 197
Strength Pareto Evolutionary Algorithm
  Zitzler, E. & Thiele, L. An evolutionary algorithm for multiobjective optimization: The strength Pareto approach Zurich, Switzerland: Computer Engineering and Networks Laboratory (TIK), Swiss Federal Institute of Technology (ETH), 1998